## Slide 1
Convective Heat Transfer in Porous Media filled with Compressible Fluid subjected to Magnetic Field
Watit Pakdee* and Bawonsak Yuwaganit
Center R & D on Energy Efficiency in Thermo-Fluid Systems
Department of Mechanical Engineering
Faculty of Engineering, Thammasat University
Thailand
*pwatit@engr.tu.ac.th

## Slide 2
Outline
1. Introduction and Importance
2. Problem description
3. Mathematical Formulations
4. Numerical Method
5. Results and Discussions
6. Conclusions

## Slide 3
1. Introduction / Importance
Magnetic field is defined from the magnetic force on a moving charge. The induced force is perpendicular to both velocity of the charge and the magnetic field.
Magnetohydrodynamic (MHD) refers to flows subjected to a magnetic field.
Analysis of MHD flow through ducts has many applications in design of generators, cross-field accelerators, shock tubes, heat exchanger, micro pumps and flow meters [1].
[1] S. Srinivas and R. Muthuraj (2010) Commun Nonlinear Sci Numer Simulat, 15, 2098-2108.

## Slide 4
1. Introduction / Importance
MHD generator and MHD accelerator are used for enhancing thermal efficiency in hypersonic flights [2], etc.
In many applications, effects of compressibility / variable properties can be significant, but no studies on MHD compressible flow in porous media with variable fluid properties have been done.
We propose to investigate the MHD compressible flow with the fluid viscosity and thermal conductivity varying with temperature in porous media.
[2] L. Yiwen et.al. (2011) Meccanica, 24, 701-708.

## Slide 5
d
2. Problem Description
2D Unsteady flow in pipe with isothermal no-slip walls through porous media
Transverse magnetic field
Porosity = 0.5

## Slide 6
2. Mathematical Formulation
The governing equations include conservations of mass, momentum and energy for electrically conducting compressible fluid flow under the presence of magnetic field.
The Darcy-Forchheimer-Brinkman model represents fluid transport through porous media [1].
Hall effect and Joule heating are neglected [2].
[1] W. Pakdee and P. Rattanadecho (2011) ASME J. Heat Transfer, 133, 62502-1-8.
[2] O.D. Makinde (2012) Meccanica, 47, 1173-1184.

## Slide 7
2. Mathematical Formulation
2.1 Conservation of Mass
where and grad

## Slide 8
2.2 Conservation of Momentum
X-direction
Y-direction
2. Mathematical Formulation
Magnetic field strength
Electrical conductivity
Permeability

## Slide 9
2.3 Conservation of Energy
2. Mathematical Formulation

## Slide 10
2.4 Stress tensors
2.5 Viscosity
2. Mathematical Formulation

## Slide 11
2.6 Effective thermal conductivity (keff)
2.7 Total energy (et)
2.8 Ideal gas Law
,
2. Mathematical Formulation

## Slide 12
3. Numerical Method
Computational domain 2 mm x 10 mm with 29 x 129 grid resolution
Sixth - Order Accurate Compact Finite Difference is used for spatial discritization.
The solutions are advanced in time using the third - order Runge – Kutta method.
Boundary conditions are implemented based on the Navier-Stokes characteristic boundary conditions (NSCBCs) [3]
[3] W. Pakdee and S. Mahalingam (2003) Combust. Teory Modelling, 9(2), 129-135.

## Slide 13
Time evolution of velocity distribution (Strength of magnetic field of 780 MT & Reynolds number of 260)
1)
2)
3)
4)
3. Results

## Slide 14
1)
2)
3)
4)
Time evolution of temperature distribution (Strength of magnetic field of 780 MT & Reynolds number of 260)
3. Results

## Slide 15
Time evolutions of velocity and temperature distributions at x = 5 mm
3. Results
Velocity
Temperature

## Slide 16
Comparisons: With vs. Without Magnetic field
3. Results
Effect of Lorentz force

## Slide 17
3. Results
Velocity fields and temperature distributions are computed
They are compared with the work by Chamkha [4] for incompressible fluid and constant thermal properties.
Variations of variables are presented at different Hartmann Number (Ha) which is the ratio of electromagnetic force and viscous force.
[4] Ali J. Chamkha (1996) Fluid/Particle Separation J., 9(2),129-135.

## Slide 18
3. Results
Velocity field at different Hartmann numbers
Present work
Previous work [4]

## Slide 19
3. Results
Temperature distributions at different times
Present work
Previous work [3]

## Slide 20
5. Conclusions
Heat transfer in compressible MHD flow with variable thermal properties has been numerically investigated.
The proposed model is able to correctly describe flow and heat transfer behaviors of the MHD flow of compressible fluid with variable thermal properties.
Effects of compressibility and variable thermal properties on flow and heat transfer characteristics are considerable.
Future work will take into account of variable heat capacity. Also effects of porosity will be further examined.

## Slide 21
Thank you for your attention