## Slide 1
II. Emerging resources and technologies

## Slide 2: Challenges and perspectives in producing solar fuels from CO2 and H2O
Univ. Messina INSTM
Dip di Ing. Elettr.onica, Chimica ed Ing Industriale, Univ. Messina, ERIC aisbl and CASPE (INSTM Lab of Catalysis for Sustainable Prod and Energy) e:mail: centi@unime.it
G. Centi and S. Perathoner
II. Emerging resources and technologies

## Slide 3: Summary /Concepts presented
Introduction
  Solar fuels and the energy infrastructure (renewable energy - RE)
  Need to store and transport RE (energy vectors)
  Solar fuels from CO2: impact on GHG and to enable RE
  Solar fuels to move to a sustainable chem. prod. scenario
Short-medium term (5 years)
  multistep production of methanol and other fuels
Medium-long term (15 years)
  develop artificial leaves (move to Economy 3.0)
Conclusions
few glimpses

## Slide 4: Germany Energy Plant
Renewable in 2050 will provide > 85% of electricity
Denmark energy plan: 100% RE in 2050
Pathways to 100% RE

## Slide 5: Technol. issues to increase use of RE
Intermittency
  Storage
    improved systems for energy storage
    devices for chemical energy conversion
Potential unexploited RE sources
  A large part cannot be actually exploited
    not-local uses, too remote for transport
Using RE in process industry
  convert renewable to chemical energy
  produce raw materials for (chemical) industry

## Slide 6: RE (wind, solar) production intermittency
Due to intermittency in RE production,
Already a part of the produced RE cannot be introduced in the grid (average full load use wind 40%)
Without efficient systems for storage it is not possible to further increase the use of RE
Changes during days
Changes within one day
Wind energy report Germany 2011 FRAUNHOFER INST IWES
Smart grids are only a partial solution (effective on local scale)

## Slide 7: Technol. issues to increase use of RE
Intermittency
  Storage
    improved systems for energy storage
    devices for chemical energy conversion
Potential unexploited RE sources
  A large part cannot be actually exploited
    not-local uses, too remote for transport
Using RE in process industry
  convert renewable to chemical energy
  produce raw materials for (chemical) industry

## Slide 8: Hydropower potential
Hydropower development ratio for world regions and top five countries with
the highest potential
Countries with largest developed proportion of their hydro potential (countries with hydropower prod. > 30 TWh/yr)
Data source: WEC Survey of Energy Resources 2007, IEA Renewables Information 2010
Much larger potential of hydropower, but to fully enable these possibilities it is necessary to transport energy at long distance

## Slide 9: Technol. issues to increase use of RE
Intermittency
  Storage
    improved systems for energy storage
    devices for chemical energy conversion
Potential unexploited RE sources
  A large part cannot be actually exploited
    not-local uses, too remote for transport
Using RE in process industry
  convert renewable to chemical energy
  produce raw materials for (chemical) industry

## Slide 10: Introduce RE in chemical prod./process ind.
  a critical element to decrease the carbon and environmental footprint
  renewable energy  produce electrical energy as output (except biomass) in a discontinuous way
    problem to couple with Chem Prod./process Ind.
  Electrical energy does not well integrate into chemical production, except as utility.
    chemical processes: based on the use of heat as the source of energy for the chemical reaction, apart few processes
    In the chemical sector, on the average only 20% of the input energy is used as electrical energy (including that generated on-site) to power the various process units and for other services.

## Slide 11: Technol. issues to increase use of RE
Intermittency
  Storage
    improved systems for energy storage
    devices for chemical energy conversion
Potential unexploited RE sources
  A large part cannot be actually exploited
    not-local uses, too remote for transport
Using RE in process industry
  convert renewable to chemical energy
  produce raw materials for (chemical) industry
Use of CO2

## Slide 12: Solar fuels
Concept of solar fuels
  energetic molecules obtained from the use of renewable energy sources and which avoid the use of fossil fuels for energy applications.
  Simpler solar fuel is H2 (renewable H2)
  BUT the actual trend is to produce liquid fuels
    can be easier stored and transported to long distance.
Role of CO2
  the fuels which can be produced from CO2 and ren.H2 (methanol, DME, hydrocarbons, etc.) are the preferable energy vectors which integrate well into the actual energy infrastructure (eg. low investments for transition)
G. Centi, S. Perathoner, ChemSusChem 2010, 3, 195-208.
G. Centi, S. Perathoner, Greenhouse Gases: Science and Techn. 2011, 1, 21–35.

## Slide 13: New scenario for sustainable chem. prod.
New raw materials and green energy for chemical production value chain
G. Centi, S. Perathoner, ChemSusChem 2013 (subm.)
CO2 and (waste) biomass are the raw materials resources of Europe

## Slide 14: CO2 utilization
Realize energy efficiency
  A resource & energy efficiency chemical production
    reduce use fossil fuels as raw material AND energy vectors
    introduce renewable energy in the chemical production chain
  Import unexploited renewable energy (RE) resources
    via renewable H2 (water electrolysis) using remote RE sources and CO2 conv. to methanol or other CO2-derived energy vectors
    produce solar fuels and chemicals
  Local storage on RE in smart grids
    Power-to-gas (CO2 to CH4)
  Develop artificial leaves
    in a long-term, for distributed production

## Slide 15: CO2/RE: relevant and cost-effective route
reduced emissions of both pollutants (NOx, etc.) and greenhouse gases
  use of unexploited renewable energy sources reduces the need of new power plants as well as of extraction of fossil fuels
better diversification of energy resources and greater flexibility in use
  with benefits in terms of energy security; methanol or DME can be used to produce components for the transport sector, for example
better flexibility in energy management to follow fluctuating energy demand,
  methanol-fuelled turbine have a rapid switch off-on time; methanol is considered a superior turbine fuel (even if the system must be modified), with low emissions, excellent heat rate, and high power output.
further benefits

## Slide 16: Paths to link CO2 and RE for chem./energy industry
CO2 as a valuable carbon source
  CO2 to olefins
CO2 as energy vector for remote (or underused) electrical energy sources
  CO2 to methanol
    techno-economic estimations
  Formic acid to transport H2
  Power-to-gas
Solar fuels from CO2 and H2O
  Going to artificial leaves

## Slide 17
CO2 re-use scenario: produce CH3OH using cheap ee in remote areas
CO2
CH3OH
An efficient (and economic) way to introduce renewable energy in the chemical production chain
H2
H2
CH3OH
CH3OH
An alternative (and more effective for chem. ind.) way to CCS
17
Improved electrocatalysts (reduce overpotential)
New catalysts for CO2 to methanol (role H2O)
Catalysts to be used in microreactors
CO2 cargos for Carbotube 75

## Slide 18: Simplified block diagram of different material flows participating into the process of methanol synthesis from CO2 and renewable H2.
two stages methanol synthesis from CO2

## Slide 19: Cost of CH3OH from CO2 (remote ee/ren. H2)
Sensitivity analysis of the methanol production cost from CO2 and renewable H2 as a function of four main parameters. The cost estimated for the base reference case and the actual range (Aug. 2013) for contract price of methanol in Europe are also indicated.
WACC: Weighted Average Cost of Capital
cCO2 at site: cost of CO2 at site (related to recovery),
NPI: new plant investment cost
EC H2: electricity consumption for the H2 production

## Slide 20: CO2 current vs. potential future chem. use
current uses
potential future uses
but a VIRTUAL CO2 that derives from NH3 (H2) synthesis
CO2 co-feed with syngas
current physical use, can be increased by EOR
potential saving CO2 eq.(world scale) (use 10PWh unexploited RE)
potential (world scale) (~15% olefin world prod.)
2 Mtons CO2  ~ 5 Mtons polymers
0,2 Mtons CO2  ~ 0,8 Mtons chemicals

## Slide 21: Comparison of the CO2/RE path with CCS and biofuels
CCS ~ 600 Mt CO2
  effective contribution nearly half  energy need for CO2 capture, transport and storage
biofuels ~ 700 Mt CO2
  lower if considering land change use & other aspects
CO2/RE: potential impact > 800 Mt CO2
  15% of unexploited RE, includes about 0.2 tons CO2 per ton CO2 eq. of energy for the conv. to methanol; the impact is related to avoided CO2 by introducing RE in the energy chain
estimation for Europe, by 2050
IEA: Energy Technology Perspective 2012
BLUE Map targets
(2.1 Gt CO2-eq. by 2050 on global scale)
CO2/RE is an effective solution to contribute to mitigate on climate change

## Slide 22: Comparison of the CO2/RE path with CCS and biofuels
CCS
  average 60€/ton captured
  tot. cost in year 2050 per 1Gt CO2 removed EU  60 B€
biofuels
  IEA (BLUE Map Scenario): "... Between 2030 and 2050, total incremental costs for biofuels are around US$ 330 billion in the high-cost scenario..." (oil at US$ 120/bbl in 2050)
  tot. cost in year 2050 per 1Gt CO2 removed  35 B€
CO2/RE
  considering 20€/ton subsidies to make methanol cost eq. to fuel projected cost
  tot. cost in year 2050 per 1Gt CO2 removed  20 B€
estimated costs (Europe)
CO2/RE is the cost-effective solution for GHG emission reduction

## Slide 23: A CO2 roadmap
2012 2020 2030
ee
excess electrical
energy (discont.,
remote,...)
H2
CH3OH, DME, olefins, etc.
electrolyzers
(PEM)
catalysis
in chemical industry to increase use of renewable energy
PEC
H2 prod.
(Conc. solar,
bioH2,...)
H2
CH3OH, DME, olefins, etc.
catalysis
ee
inverse (methanol)
FC
CH3OH, DME, olefins, etc.
distributed energy
artificial
leaves
G. Centi, S. Perathoner et al., ChemSusChem, 2012

## Slide 24: New routes for producing renewable H2
bio-route using cyanobacteria or green algae
high temperature thermochemical one using concentrated solar energy
photo(electro)chemical water splitting or photoelectrolysis using semiconductors
The low temperature approach (PEC solar cell) has a greater potential productivity in solar fuels per unit of area illuminated AND may be used also for C-based energy vector
Centi,, Perathoner, ChemSusChem, 3 (2010) 195.
productivities in H2 formation from water splitting per unit of surface area irradiated

## Slide 25: Integrating the stages in CO2 conversion
inverse (methanol) fuel cells
ee
Formally analogous, BUT new type of electrocatalysts are requires (cell and electrode engineering remains similar)

## Slide 26: Towards artificial leaves
Helios SERC
Still mainly at the conceptual design
CalTech (Lewis research group).

## Slide 27: Toward artificial leaves
1st generation cell
2nd generation cell
G. Centi, S. Perathoner et al., ChemSusChem, 2012

## Slide 28: Vision 2050: CO2/artificial leaves
Provide a delocalized energy
  to smart cities and buildings
  for mobility and industry
C
O
O
O
O
C
artificial leaf
Light reaction
2H2O  O2 + "2H2"
Dark reaction
"2H2" + CO2  (CH2O)
(liquid HC, alcohols)

## Slide 29: CO2/Artificial Leaves
EU challenge

## Slide 30: Conclusions
(re)using CO2 to produce solar fuels can be a disrupting (game changer) opportunity for Europe and to meet societal challenges
  large potential (Gtons CO2 eq.) to exploit unused renewable energy resources, contributing to meet GHG targets, decreasing impact on environment and improving energy security
  open new scenario for sustainable chemical production and energy, with increase in competiveness, innovation and jobs
base economic elements indicate feasibility
  the development of related technologies/catalysts/materials will be a main driver for innovation  combine efforts in Europe to win this race
in a long term the vision is to develop artificial photosynthesis (artif. leaves)
  bio-inspired, with higher productivity and tailored conversion of CO2
  Economy 3.0 (direct, delocalized energy production)
ISBN: 978-3-11-027729-6
ISBN: 978-1-118-59088-1
ISBN: 978-1-4471-5118-0