## Slide 1
EU-wide studies on the integration of
renewable energies in the electricity grid
F. Wagner, IPP Greifswald
1
Exemplified first
on the basis of German data
then with EU-wide data
Germany
Load:
varies between 80 and 40 GW
RES 2014:
installed wind power: ~ 35 GW installed PV power: ~ 35 GW

## Slide 2
Sources for electricity
– today and „tomorrow“
2
EU-wide studies on the integration of
renewable energies in the electricity grid
F. Wagner, IPP Greifswald
Exemplified first
on the basis of German data
then with EU-wide data
Germany
Load:
varies between 40 and 80 GW
RES 2014:
installed wind power: ~ 35 GW installed PV power: ~ 35 GW
100%, optimal mix case
level of
consumption
unchanged
500 TWh

## Slide 3
Method and assumptions
Method:
Take load-, wind-, PV-… data from 2012 and scale the intermittent RES
to higher capacities e.g. to the 100% case )
Assumptions:
no savings in electricity consumption
hydro remains the same, subtracted from load →
no nuclear power
no biogas
no losses
The mix of wind and PV follows the
optimal mix: ~ 80% energy from wind, ~20% energy from PV
100% case
reduced load
optimal mix
3

## Slide 4
How much RES power has to be installed? The remaining need for back-up power? The extent of surplus energy? Dimensioning storage? The dynamics of the back-up system? The conditions for DSM (demand-side management)? | The amount of CO2 reduction? Conditions of a 100% supply by RES? What could be a reasonable share by intermittent RES? The benefits of an EU-wide use of RES Costs of RES?
Topics:
Special topics:
Sweden: is it possible to replace nuclear power by wind
Japan: the role of PV with a second demand peak in summer
4

## Slide 5
The basic problem of intermittent sources
Annual duration curves of load and wind+PV under optimal mix
power (MW)
time (months)
load

## Slide 6
How much power has to be installed? Enough to serve Europe in good days The remaining need for back-up power? 88% The extent of surplus energy? Formally enough to serve Poland Dimensioning storage? For a 100% case: 33 TWh The dynamics of the back-up system? From 0 up to the load; strong gradients The conditions for DSM (demand-side management)? Cheap electricity prices during the day | The amount of CO2 reduction? Not to the level of France, Sweden... Conditions of a 100% supply by RES? Use of biogas (e.g. 40 TWh) and savings (to 30%) What could be a reasonable share by intermittent RES? 40% The benefits of an EU-wide use of RES? Effects in the order of 20-30% Costs to implement RES? high
Major Results
6

## Slide 7
Chart: 
the last 8 weeks in 2012
Maximum power
of back-up system
power (MW)
Base load
The power of the back-up system remains high
It has to meet the full dynamic range from 0 to nearly peak load
The power gradients increase strongly
7
Results in more detail: Back-up system

## Slide 8
Chart: 
Storage
power (MW)
Mo 9.1.2012 – Su 12.2.2012
black: load
red: back-up
blue, negative: surplus
8
Jan / Feb 2012
100%, optimal mix case

## Slide 9
Chart: 
power (MW)
Mo 9.1.2012 – Su 12.2.2012
9
h | 66 | 90 | 117 | 67 | 27 | 71 | 70 | 83
TWh | 3.7 | -3.5 | 4.5 | -2.5 | 0.5 | -2.4 | 0.8 | -3.4
Storage

## Slide 10
Chart: 
0
2
4
6
storage level (TWh)
power (MW)
Mo 9.1.2012 – Su 12.2.2012
h | 66 | 90 | 117 | 67 | 27 | 71 | 70 | 83
TWh | 3.7 | -3.5 | 4.5 | -2.5 | 0.5 | -2.4 | 0.8 | -3.4
10
Storage

## Slide 11
Chart: 
0
2
4
6
empty
power (MW)
Mo 9.1.2012 – Su 12.2.2012
storage level (TWh)
11
h | 66 | 90 | 117 | 67 | 27 | 71 | 70 | 83
TWh | 3.7 | -3.5 | 4.5 | -2.5 | 0.5 | -2,4 | 0.8 | -3.4
181
-7.1
Storage

## Slide 12
Chart: 
0
2
4
6
power (MW)
Mo 9.1.2012 – Su 12.2.2012
12
h | 66 | 90 | 117 | 67 | 27 | 71 | 70 | 83
TWh | 3.7 | -3.5 | 4.5 | -2.5 | 0.5 | -2,4 | 0.8 | -3.4
181
-7.1
storage level (TWh)
Storage

## Slide 13
Chart: 
0
2
4
6
power (MW)
Mo 9.1.2012 – Su 12.2.2012
storage level (TWh)
13
h | 66 | 90 | 117 | 67 | 27 | 71 | 70 | 83
TWh | 3.7 | -3.5 | 4.5 | -2.5 | 0.5 | -2,4 | 0.8 | -3.4
181
-7.1
Storage capacity
in the order of
10 TWh
storage level (TWh)
Storage

## Slide 14
Need from residual back-up depending on the storage capacity
Storage
14

## Slide 15
Countries with hydro + nuclear are already where others would like to be in 2050
Specific CO2 emission
15

## Slide 16
Countries with hydro + nuclear are already where others would like to be in 2050
Specific CO2 emission
16

## Slide 17
Conditions of a 100% supply by RES
17
Main knobs: savings/efficiency + use of biomass
Minor knobs: decrease of population, import (depatchable power?)
factor of demand reduction

## Slide 18
Possible contribution by intermittent sources
possible
limit
18

## Slide 19
Annual duration curves for German RES field (dashed) and EU-wide RES field
Benefit from an EU-wide RES field
19
Data from:
Belgium
Czech Republic
Denmark
France
Germany
Ireland
Spain
Sweden
UK

## Slide 20
the back-up energy is reduced by 24%,
the maximal back-up power by 9%,
the maximal surplus power by 15%,
the maximal grid power by 7%,
the typical grid fluctuation level by 35%
the maximal storage capacity by 28%
The benefit
20

## Slide 21
Germany
France
UK
Spain
Belgium
Czech Rep.
Denmark
Ireland
100%
The structure of the EU-wind field
normalised surplus
and
„useful“ surplus
21
wind
correlation
coefficient

## Slide 22
Interconnector capacity
22

## Slide 23
Source: F. Wagner
Finadvice
Development costs
23

## Slide 24
Sweden
load | wind | Hydro | Nuclear | Bio-mass
134 TWh | 10 TWh | 62 TWh | 64 TWh | 8.1 TWh
w/o nuclear power
present situation
on the basis of
the first two weeks
in November 2013
24

## Slide 25
Sweden
At constant hydropower:
(1) 9 GW nuclear → 63.8 TWh
or
22.3 GW wind + 8.6 GW back-up → 64,8 TWh.
With gas: Increase in CO2-emission by 50%.
Additional issues:
PV cannot replace the fossil back-up
Too little surplus, thanks to hydropower, to replace the back-up by pumped storage
25

## Slide 26
Japan
J F M A M J J A S O N D
time (months)
power (MW)
Load variation with
summer and winter peak
The share of
PV power
26
The second peak – due to summer AC: does not change the optimal mix

## Slide 27
Conclusions
Large installations: high costs
Use of landscape
Only 12% savings in back-up
Uneconomic use of back-up (little operation, high maintenance costs)
Technology for large-scale storage not developed
Storage will not be economic
Large price difference between primary and secondary electricity
DMS will force the weekends to be used for economic purposes
Nuclear power is more efficient to reduce CO2 emission
Possibly, 40% of intermittent electricity tolerable: The rest?

## Slide 28
Dt: costs
The German „Energiewende“
28
One has to discriminate between
the aims
and the selected route

## Slide 29
from red: fossil, nuclear
to blue: wind, PV
Along the way:
Increase in world population
Increase of CO2
Increase in energy consumption
  Other issues: Oil-peak
  Economic disparities
  Politically caused shortages
  Destruction of supply infrastructure
  Breakthroughs in new technologies
now
2050
Dt: costs
The German „Energiewende“
29

## Slide 30
from red: fossil, nuclear
to blue: wind, PV
Along the way:
Increase in world population
Increase of CO2
Increase in energy consumption
  Other issues: Oil-peak
  Economic disparities
  Politically caused shortages
  Destruction of supply infrastructure
  Breakthroughs in new technologies
now
2050
Dt: costs
The German „Energiewende“
30
Keep all
options open !

## Slide 31
Mix between wind and PV, onshore and offshore wind
optimal
mix

## Slide 32
Use weekends!
Demand-side-management

## Slide 33
Full integration of weekends:
Additional use of RE: 7.9 TWh
Peak-load: 83 → 63 MW
Reduction of back-up system:
131 → 123 TWh
33
Mo
Tue
We
Th
Fr
Sa
Su
Demand-side-management: use of weekends

## Slide 34
Pair of countries | R
Germany-Czech Rep. | 0.53
Germany-Denmark | 0.56
Germany-France | 0.45
Germany-UK | 0.40
Germany-Belgium | 0.39
Germany-Sweden | 0.37
Germany-Ireland | 0.19
Germany-Spain | 0.05