## Slide 1
Surplus from and storage of electricity generated by intermittent sources
F. Wagner Max-Planck-Institut für Plasmaphysik, Greifswald, Germany
Goal:
Assess variability from year to year: 2010, 2012, 2013, 2015
Principles: use data of a year and scale them to so called 100%, optimal mix case
The optimal mix
1

## Slide 2
 | 2010 | 2012 | 2013 | 2015
production Won TWh | 262 | 271 | 270 | 258
production Woff TWh | 131 | 135 | 136 | 129
production PV TWh | 107 | 94 | 94 | 113
production back-up/surplus TWh | 136 | 131 | 137 | 122
installed power Won GW | 188 | 176 | 183 | 117
installed power Woff GW | 39 | 33 | 33 | 53
installed power PV GW | 142 | 97 | 109 | 128
installed power back-up GW | 75 | 73 | 72 | 73
full-load-hour flh h | 986 | 1209 | 1114 | 1270
capacity factor cf % | 11 | 14 | 13 | 14
utilisation factor uf % | (70) | 59 | 60 | 57
Year-to-year comparison
For given installed power electricity generation can vary by 30 %
2
Generation by iRES: 500 TWh

## Slide 3
Week with largest surplus
26.3. to 1.4.2012
Week with largest back-up
12.-18.11.2012
500 TWh generated
369 TWh (74%) directly used
153 TWh (41%) at a power level below or equal to the load
216 TWh (59%) with p above the load → the need for surplus production
3
The extreme cases

## Slide 4
The electricity export
strongly increases.
Numerically, the export
agrees with the PV
energy generated
Surplus production today in form of export

## Slide 5
Back-up power
Surplus power
5
Power distribution

## Slide 6
2012
2010
2013
2015
For 171 h power < 10% of the respective load
16 h with duration lower than 1 h
98 h with duration between 1 and 6 h
57 h with duration between 6 and 12 h.
6
Partitioning of annual duration curve

## Slide 7
fop = ratio of overproduction to target energy (500 TWh)
fp = peak grid power to peak power of the load (83 GW in 2012).
7
180 GW
131 TWh
190 TWh
Consequences of curtailing power peaks

## Slide 8
Onshore wind contribution drops from 271 to 149 TWh → importance of Won.
The Won capacity factor drops from 0.18 to 0.08
Remaining surplus: 9.7 TWh.
8
Curtailing onshore wind whenever piRES above load

## Slide 9
Daily variation of
average surplus power
total: 131 TWh
During the day: 83 TWh
Average per day: 0.23 TWh
Maximum: 1.2 TWh
Standard deviation: 0.29 TWh
Strategy:
Shift surplus from day into night
9
Conditions for demand-side-managment
Maximum during the day

## Slide 10
Variation of surplus energy
during the day 6:00 – 18:00
and during the night
Variation of surplus power
for 3 weeks in April 2012
Red: average
No surplus for 134 days (2012)
The day-to-day variation seem to be too large to base repetitive
processes on the DSM concept
10
Conditions for demand-side-managment

## Slide 11
Surplus – back-up from
9:30 to 18:00 : 0.1 TWh.
daily demand :1.36 TWh
average daily surplus : 0.36 TWh
1/3 of it can be moved from the
day to the night
11
Viability of day storage

## Slide 12
Daily surplus energies for two months in winter (January and February 2012)
for two in summer (July and August) split into the day and the night periods.
In winter: strong correlation between day and night → no transfer
12
Viability of day storage

## Slide 13
reduced load, back-up and surplus power shown for three cases
the day (2.4.12) with the largest energy transfer from the storage to the grid
the one (15.11.12) with the largest back-up need
the one (31.12.12) with the largest surplus energy
Daily storage with 0.36 TWh = average daily surplus energy in 2012
Work done in 195 days: 21.7 TWh
Surplus power on April 2nd with the largest transfer: 80 GW
capacity factor: 3%
13
Viability of day storage

## Slide 14
filling level strongly depends
on the weather conditions
The storage capacity varies
between 26 TWh (2013) and
46 TWh (2015)
Storage empty in fall
14
Seasonal storage (ideal case)

## Slide 15
2012, no losses
electricity → H2
(h = 0.8)
electricity → H2 → electricity
(0.6)
electr. → H2 → CH4 → electr.
(0.4)
Seasonal storage loses character:
short operational periods
after bursts of surplus
15
Seasonal storage (with losses)

## Slide 16
I doubt that there will be
storage to close the
electricity loop with
intermittent RES
16
Seasonal storage (with losses)

## Slide 17
General features of overproduction:
Saturation of directly used energy
17
Direct energy gain DE by
adding 10 GW to the stock
Concept: allow overproduction > 500 TWh

## Slide 18
Strong decrease of storage
capacity, because
used energy approaches
500 TWh target
fRES = 2: 55 TWh missing,
irrelevant
But: at the expense of large
overproduction
18
Concept: allow overproduction > 500 TWh

## Slide 19
19
fRES = 1
Best use of surplus: heating

## Slide 20
GHG emission (Mill t/y)
expected development
with present regulations
if lignite had been
removed instead
of nuclear power
if 2011 all coal power
stations had been
replaced by gas
2025
target
20
CO2, GHG development, past and expected