## Slide 1
MYRRHA
Multipurpose hYbrid Research Reactor for High-tech Applications
Contributing to the 3rd Pillar of the European Strategy for HLW Mgt through P&T
Open for international participation
Marc Schyns
SCK•CEN, Boeretang 200, 2400 Mol, Belgium
mschyns@sckcen.be or myrrha@sckcen.be
3th European Energy Conference – 28-30 October 2013 – Budapest

## Slide 2: MYRRHA - Accelerator Driven System
Reactor
Subcritical or Critical modes
65 to 100 MWth
Accelerator
(600 MeV - 4 mA proton)
Fast
Neutron
Source
Spallation Source
Lead-Bismuth
coolant
Multipurpose
Flexible
Irradiation
Facility
Innovative & Unique

## Slide 3: MYRRHA Accelerator Challenge
fundamental parameters (ADS) | 
particle | p
beam energy | 600 MeV
beam current | 4 mA
mode | CW
MTBF | > 250 h
implementation | 
superconducting linac | 
frequency | 176.1 / 352.2 / 704.4 MHz
reliability = redundancy | double injector
 | “fault tolerant” scheme
failure = beam trip > 3 s
challenge !

## Slide 4: About beam trips

## Slide 5: MYRRHA linac

## Slide 6: Reactor layout
Reactor Vessel
Reactor Cover
Core Support Structure
  Core Barrel
  Core Support Plate
  Jacket
Core
  Reflector Assemblies
  Dummy Assemblies
  Fuel Assemblies
Spallation Target Assembly and Beam Line
Above Core Structure
  Core Plug
  Multifunctional Channels
  Core Restraint System
Control Rods, Safety Rods, Mo-99 production units
Primary Heat Exchangers
Primary Pumps
Si-doping Facility
Diaphragm
  IVFS
IVFHS
  IVFHM

## Slide 7: Core and Fuel Assemblies
151 positions
37 multifunctional plugs

## Slide 8: Core and Fuel Assemblies
Fuel
  Cladding in 15-15 Ti
  Wire wrap
  Wrapper in T91

## Slide 9: Cooling systems
Decay heat removal (DHR) through secondary loops
  4 independent loops
  redundancy (each loop has 100% capability)
  passive operation (natural convection in primary, secondary and tertiary loop)
Ultimate DHR through RVCS (natural convection)

## Slide 10: Integration into building

## Slide 11: Multipurpose facility ADS demonstration & P&T Research
Multipurpose
hYbrid
Research
Reactor for
High-tech
Applications
Waste
Fission GEN IV
Fusion
Fundamental
research
Silicon
doping
Radio-
isotopes
50 to 100 MWth
FFast = ~1015 n/cm².s
(En>0.75 MeV)
F = 1 to 5.1014 n/cm².s
(ppm He/dpa ~ 10)
in medium-large volumes
Material research
FFast = 1 to 5.1014 n/cm².s
(En>1 MeV) in large volumes
Fuel research
Φtot = 0.5 to 1.1015 n/cm².s
Fth = 0.5 to 2.1015 n/cm².s
(En<0.4 eV)
Fth = 0.1 to 1.1014 n/cm².s
(En<0.4 eV)
High energy LINAC
600 MeV – 1 GeV
Long irradiation time

## Slide 12: Motivation for transmutation
spent fuel reprocessing
no reprocessing
Uranium
naturel
Time (years)
Relative radiotoxicity
transmutation
of spent fuel
Duration Reduction 1.000x
Volume Reduction 100x

## Slide 13: European Strategy for P&T
The implementation of P&T of a large part of the high-level nuclear wastes in Europe needs the demonstration of its feasibility at an “engineering” level. The respective R&D activities could be arranged in four “building blocks”:
  Demonstration of the capability to process a sizable amount of spent fuel from commercial LWRs in order to separate plutonium (Pu), uranium (U) and minor actinides (MA),
  Demonstration of the capability to fabricate at a semi-industrial level the dedicated fuel needed to load in a dedicated transmuter (JRC/ITU),
  Design and construction of one or more dedicated transmuters,
  Provision of a specific installation for processing of the dedicated fuel unloaded from the transmuter, which can be of a different type than the one used to process the original spent fuel unloaded from the commercial power plants, together with the fabrication of new dedicated fuel.

## Slide 14: Fast Neutron are unavoidable for transmutation
To transmute MAs, we need to fission them
The ration Fission/Capture is more favourable with fast neutrons

## Slide 15: Is sub-criticality a luxury?
Proton Beam
Spallation Target
accelerator
Both Critical reactors as well as ADS can be used as MAs transmuters
Nevertheless, critical reactors, heavily loaded with MAs, can experience severe safety issue due to reactivity effet induced by a smaller fraction of delayed neutrons.
ADS can operate in a more flexible and safer manner even if heavily loaded with MAs hence leading to efficient transmutation therefore we say that sub-criticality is not a luxury but a necessity.

## Slide 16: Why sub-criticality is needed
Proton
Accelerator
Subcritical
Neutron
Multiplier
Spallation
Source
p
n
ADS is presently studied for the MAs transmutation due to their smaller fraction of delayed neutrons and their impact of the kinetics parameters of the reacteur
235U 650 pcm 238U 1480 pcm
238Pu 120 pcm 239Pu 210 pcm
240Pu 270 pcm 241Pu 490 pcm
242Pu 573 pcm 237Np 334 pcm
241Am 113 pcm 243Am 208 pcm
242Cm 33 pcm 244Cm 100 pcm
If one wants to have a heavily loaded core (>10%), one needs to considère ADS

## Slide 17: ADS is the most efficient system for burning MAs
MA Production Rate (grams / GWh)
Pu Production Rate (grams / GWh)
* Mike Cappiello, (LANL), “The Potential Role of Accelerator Driven Systems in the US”, ICRS-10/RPS’2004, Madeira (PT), 2004

## Slide 18: Even with completely different national NE policies European solution for HLW works with ADS
Advantages for A
ADS shared with B
ADS burn A’s Pu& MA
Smaller Fu-Cycle units & shared
Scenario 1 objective: elimination of A’s spent fuel by 2100
A = Countries Phasing Out, B = Countries Continuing
SHARED

## Slide 19: But MYRRHA is more than research on ADS & Transmutation

## Slide 20: Multipurpose facility
Multipurpose
hYbrid
Research
Reactor for
High-tech
Applications
Waste
Fission GEN IV
Fusion
Fundamental
research
Silicon
doping
Radio-
isotopes
50 to 100 MWth
FFast = ~1015 n/cm².s
(En>0.75 MeV)
F = 1 to 5.1014 n/cm².s
(ppm He/dpa ~ 10)
in medium-large volumes
Material research
FFast = 1 to 5.1014 n/cm².s
(En>1 MeV) in large volumes
Fuel research
Φtot = 0.5 to 1.1015 n/cm².s
Fth = 0.5 to 2.1015 n/cm².s
(En<0.4 eV)
Fth = 0.1 to 1.1014 n/cm².s
(En<0.4 eV)
High energy LINAC
600 MeV – 1 GeV
Long irradiation time

## Slide 21: Material Irradiation Performances for FRs Critical@100 MW
 | IPS in Chan [0 0 0] |  | IPS in Chan [2 0 0] | 
Sample n° | dpa/EFPY | Φtot | dpa/EFPY | Φtot
8 | 18.1 | 2.38E+15 | 16.2 | 2.12E+15
7 | 23.0 | 2.85E+15 | 20.7 | 2.54E+15
6 | 25.9 | 3.19E+15 | 23.3 | 2.85E+15
5 | 27.5 | 3.37E+15 | 24.5 | 3.02E+15
4 | 27.2 | 3.39E+15 | 24.5 | 3.03E+15
3 | 25.7 | 3.23E+15 | 22.9 | 2.89E+15
2 | 22.3 | 2.92E+15 | 19.9 | 2.62E+15
1 | 17.3 | 2.50E+15 | 15.5 | 2.23E+15

## Slide 22: Irradiation capabilities of IPS for FR Reactors Sub-critical @ 73 MW
IPS | Total flux, n/(cm2s) | Fast (> 0.75 MeV) flux, n/(cm2s) | Radiation damage, DPA/FPY | Helium production, appm/FPY | Ratio appm He/DPA
1 | 2.64×1015 | 4.20×1014 | 22.3 | 7.66 | 0.343
2 | 2.72×1015 | 4.29×1014 | 23.0 | 10.41 | 0.452
3 | 2.75×1015 | 4.29×1014 | 23.1 | 5.94 | 0.257
4 | 2.72×1015 | 4.18×1014 | 22.5 | 6.59 | 0.293
5 | 2.70×1015 | 4.35×1014 | 22.7 | 6.52 | 0.288
6 | 2.68×1015 | 4.23×1014 | 22.8 | 10.78 | 0.474

## Slide 23: Prepare the path for Fusion DEMO Irradiation capabilities under spallation target
+10 cm
0 cm
-30 cm

## Slide 24: MYRRHA for fusion material irradiations
Estimated damage induced in DEMO and proposed
irradiation conditions in IFMIF and MYRRHA-IMIFF

## Slide 25: Radioisotope (Mo-99) production capability Sub-critical @ 73 MW
Average specific power
173 W/cm2
184 W/cm2
171 W/cm2

## Slide 26: Radioisotope (Mo-99) production capability Critical @ 100 MW
Heat flux ≤ 400 W/cm2

## Slide 27: MYRRHA - Concept
MYRRHA - Concept
MYRRHA for fundamental research
ISOL@MYRRHA - Concept
thin refractory metal foils
carbide powders
liquid targets
surface ion source
ECR ion source
RILIS

## Slide 28: MYRRHA in the European Context
Energy
Independence
Knowledge
Economy
ESFRI
European Strategic Forum for Research Infrastructure
SET Plan
European Strategic Energy Plan
27.11.2010
Confirmed on ESFRI
priority list projects
15.11.2010
in ESNII
(SNETP goals)

## Slide 29: Belgian commitment: secured International consortium: under construction
Belgium 60 M€
(12 M€/y x 5 y)
2nd phase (11 y)
others 576 M€
Belgium 324 M€
(36 M€/y x 9 y)
Consortium
960 M€
(2009)

## Slide 30: The project schedule Executing presently the FEED Phase: 2010-2014/15
2010-2014
Front End
Engineering
Design
2019
On site
assembly
2016-2018
Construction of
components &
civil engineering
2015
Tendering &
Procurement
2020-2022
Commissioning
2023
Progressive
start-up
2024-
Full
exploitation
FEED
(Front End
Engineering
Design)
Minimise technological risks
Secure the licensing
Secure a sound management and investment structure
PDP
preliminary
dismantling
plan
PSAR
preliminary
safety
assesment
EIAR
environmental impact
assesment
Central
Project
Team
Owner
Engineering
Team
Owner
Consortium
Group
2010-2014/15

## Slide 31
MYRRHA R&D open for international collab.
Notes: 31

## Slide 32: MYRRHA Project open for International Participation
BE
EU countries
Asian country
EU
ROW
SCK•CEN
(on behalf of Belgian
Federal
Government)
EU country
Public foundation
Asian country
EU participation
ROW participation
Belgian Federal Ministry
of Energy
(50%)
Belgian Federal Ministry
of Science Policy (50%)
40 %
Major European partners
A major Asian partner
EU FP7 (RTD) / SET-Plan (Energy)
ROW
(*) European Research Infrastructure Consortium
«ERIC» (*)
Contribution to investment capital
(960 M€’09)
Participation vehicle
(Consortium members)
Primary «investors»
IPR
management rules tbd
INVESTMENT PHASE

## Slide 33: Conclusions
MYRRHA As a Multipurpose Fast Spetrum irradiation facility selected by ESFRI, is responding to:
  The issue of addressing the nuclear waste legacy of present reactor technology through advance options (ADS, P&T)
  The SNETP need for a multipurpose research infrastructure expressed in its Strategic Research Agenda whatever the considered technology for Gen.IV systems
  The Objective of Belgium and SCK•CEN to maintain a high level expertise in the country in the nuclear safety, nuclear technology and nuclear competencies independently of the future of NE
  The objective of the European Commission to make available a series of relevant irradiations facilities for the fusion material research community towards the DEMO construction
  Secure society needs for RI for medical applications and Dopped-Si for renewable Energy

## Slide 34: MYRRHA: EXPERIMENTAL ACCELERATOR DRIVEN SYSTEM A pan-European, innovative and unique facility at Mol (BE)
BR2 reactor
(existing)
MYRRHA reactor
building
MYRRHA LINAC
high energy tunnel
ECR source & Injector Building
Utilities
buildings